## Slide 1: 2024 PHYSICAL DESIGN FINAL PROJECT PROPOSAL “ CHIP LEVEL GLOBAL ROUTER “
Group11
R12943097 孫定洋 R12943117 隋中彧
R12943094 劉建亨 R12921090 温千懿
Notes: 大家好，我們是第11組，那我們這組做的主題是Chip Level Global Router

## Slide 2: OUTLINE
Introduction
Our program flow
Proposed method
Results
Notes: 那這邊是我們的outline，一開始我們會簡單介紹這次Project在做什麼，接著我們介紹我們的Program流程，再來講解一下我們是怎麼實踐的，最後會Demo我們的實驗數據。

## Slide 3: INTRODUCTION
Our main goal is to optimize these elements and output our routing layout.
In this problem, there are four elements that should be considered :
  1) Channel overflow
  2) Wirelength
  3) Edge pin density
  4) Net turn cost
Notes: 那這次Project我們做的是ICCAD的第四題， 這個Project題目簡單來說就是，在chip level 上做最佳化的繞線處理，那chip由5種元件構成，在題目規定的4個成本考量之下，有
overflow
wL
Edge pin density
4. Net turn cost

## Slide 4: DATA STRUCTURE
Notes: 以上是我們使用的資料結構

## Slide 5: OUR PROGRAM FLOW
Result
Visualization of case
Detail Routing
A*-search
Global Routing
Minimum Spanning Tree/Dijkstra
Notes: 那這邊是我們的Program Flow，一開始我們會用Minimum Spanning Tree和Dijkstra去實作global routing，接著使用A star tree實踐detail routing，接著視覺化呈現結果

## Slide 6: GLOBAL ROUTING
MST
Simply do MST on each net
“vertice” for MST : all the TX, RX of the net
“edge” for MST : E = V X V
“edge weight” for MST : simply use the Manhattan distance between the TX, RX coordinate of block given by problem
Problem : how to consider wire density ? how to avoid huge obstacle ? Also, the vertice is still to far for A* search

## Slide 7: GLOBAL ROUTING
Modified Dijkstra :
from a TX node, do Dijkstra till a shortest path to some RX node.
view the path as a supernode, relax the nodes that connect to this supernode.
While relaxation, if we found a node that is already popped out of heap but not in a path of TX, RX node. We still relax it and push it back to heap if it’s key value decrease.
from supernode, repeat previous steps till all RX is connected

## Slide 8: GLOBAL ROUTING

## Slide 9: GLOBAL ROUTING
Modified Dijkstra (following part is still on the road):
“node” : blocks + region + cut channels
  thus, all the grid available belongs to some node
“edge” : (u, v) exists if u is beside v on grid map.
“edge weight” : function of the
  wire density and capacity of u and v
  “distance” between u and v

## Slide 10: DETAIL ROUTING
Apply A*-search way to route the block.
Utilize the Manhattan Distance to calculate the cost.
The following is an example :
 |  | 6 | 6 | 6 | 6 | 6 | 
 | 7 |  | 6 | 6 | 6 | 6 | 6
 | 7 | 7 | 9 |  |  |  | 
 | 7 | 7 | 9 |  |  |  | 
 | 7 | 7 | 9 |  |  |  | 
 | 7 | 7 | 9 |  |  |  | 
 | 7 | 7 | 9 |  |  |  | 
Original A*-search
Block A
Block B
Block C
Target : Do A*-search detail routing to connect block A, block B and block C.
Notes: 經過global routing的處理後，會產生grid圖，我們使用A star search來做繞線，並利用曼哈頓距離來算出最短路徑，這邊舉簡單的小例子說明我們核心的演算法，首先經過global繞線處理後，我們知道block A會需要先經過block b，再到block c，所以綠線為計算後的最佳路徑

## Slide 11: DETAIL ROUTING
Considering Overflow and Non-throughable grids in the grid graph.
If the cost of two routes are the same, we choose the one with smaller net turns.
The following is an example :
 | 8 | 8 |  |  |  |  | 
 | 8 | 8 | 8 |  |  |  | 
 | 8 |  | 8 |  |  |  | 
 | 8 | 8 | 8 |  |  |  | 
 | 8 | 8 |  |  |  |  | 
 | 8 | 8 |  |  |  |  | 
A*-search considering overflow and non-throughable grids
Route A
Net turn: 2
Route B
Net turn: 3
Net turn of Route A is smaller than Route B
Thus, Route A is better than Route B
Overflow or Non-throughable grid
Notes: 接下來我們可能會遇到需要考慮Overflow and Non-throughable的區域，我們不會嘗試去繞的區域。以右圖為例，即灰色部分，演算法計算完後如果有兩條繞線路徑的成本相同，那我們就選擇轉彎數比較小的那條作為最佳路徑，我們會選A這條路徑

## Slide 12: VISUALIZATION OF CASE
Case 1
the density exceeds a certain value , it will turn red.
Notes: 而這是我們Case4執行完routing的結果，相近的線我就疊在一起 越密線越粗 密度超過一定值變紅線

## Slide 13: VISUALIZATION OF CASE
Case 2
Lines that are close together will overlap. The denser the line segments, the thicker they will be.
Notes: 而這是我們Case5執行完routing的結果

## Slide 14
Thanks for Listening
Notes: 那以上是我們的報告，謝謝大家